## Slide 1
قائد نمذجة معلومات البناء
BIM Leader Diploma

## Slide 2
قائد نمذجة معلومات البناء
BIM Leader Diploma
إدارة البيانات والمعلومات الرقمية
2

## Slide 3
محتويات الوحدة
CDE
1
2
3
4
إدارة البيانات والمعلومات الرقمية
3
BIM Workflow
Open BIM (IFC-COBIE)
PM– Clash Detection
قائد نمذجة معلومات البناء
BIM Leader Diploma

## Slide 4: BIM WORKFLOW & DEFINITIONS
BIM Model
BIM Workflow
Level of Development
Contractual Documents (EIR – BEP and Appendices )
CDE
BIM Standards
Open BIM (IFC - BCF)
COBie

## Slide 5: BIM MODEL
BIM Model= Information Model = Several Information Containers

## Slide 6: BIM MODEL
Federated Model = Several Information Containers

## Slide 7: REQUIREMENTS & STANDARDS
Requirements
Information
Standards

## Slide 8: BIM WORKFLOW

## Slide 10: MODELING PROCEDURE

## Slide 11: LEVEL OF DEVELOPMENT
Simulation of stairs

## Slide 12: LEVEL OF DEVELOPMENT
Level of Development
Level of detail
Level of information
Level of Detail can be thought of as input to the element, while Level of Development is reliable output

## Slide 13: LEVEL OF DEVELOPMENT
LOD Spec 2021 Part I - FINAL 2021-12-28.pdf

## Slide 14: LEVEL OF INFORMATION NEED
ISO19650 interduces
level of information need (EN 17412-
1:2020) -
It is all about purpose
Source: EN 17412-1:2020

## Slide 15
https://youtu.be/pCXTTxQgyx4?si=fgUFgfbzlkKzX9fX

## Slide 16: CONTRACTUAL DOCUMENTS (EIR – BEP & APPENDICES )
EIR
BEP
EIR & BEP Relationship

## Slide 17: EIR
It could be called
Employer Information Requirements
Exchange Information Requirements
Client BIM Protocol
Client BIM Requirements

## Slide 18: EIR
BIM Uses
Asset Information Requirements (AIR)
Modeling Strategy and Data Segregation
Naming Conventions
Security Requirements

## Slide 21: BIM EXECUTION PLAN (BEP)
How will the appointed party execute? The Plan to deliver BIM as per the EIR

## Slide 22: BIM EXECUTION PLAN (BEP)
Project Information
References/Standards
BIM Team / Stakeholders
BIM Uses
MIDP
Federation Strategy
LOIN
Clash Matrix
Naming Convention
Software
Meetings
Shared Coordinates
Checking/Validation
QA/QC
BIM view Template

## Slide 23: PROJECT INFORMATION
Project Information | Description
Project Owner: | Bonyan
Project Number | G05-002-2021
Project Name | Wezig Building
Work Type | Design
Contract Type | Lump Sum
Contract Number: | 002-2021
Other Project Information: | Wezig Building is a Mixed-use project building with one Basement and G+9 with a cantilevered first floor. Core structure with curtain wall facade envelope.
Location | Barcelona, Spain

## Slide 24: REFERENCES/STANDARDS
Standard | Usage M: Mandatory R: Recommended N/A: Not Applicable | Description | Discipline Use
ISO 19650-1:2018 | M | Organization and digitization of information about buildings and civil engineering works, including building information modeling (BIM) - Information management using building information modeling - Concepts and Principles | ARCH, STR, MEP
ISO 19650-2:2018 | M | Organization and digitization of information about buildings and civil engineering works, including building information modeling (BIM) - Information management using building information modeling - Delivery phase of the assets | ARCH, STR, MEP
BS 1192:2007 | M | Collaborative production of architectural, engineering, and construction information - Code of Practice | ARCH, STR, MEP
BS 1192-4:2014 | M | Collaborative production of information Part 4: Fulfilling Information Exchange using COBie - Code of Practice | ARCH, STR, MEP
BS 7000-4 | R | Managing construction and design | ARCH, STR, MEP
PAS 1192-3:2014 | M | Specification for information management for the operational phase of assets using building information modeling (BIM) | ARCH, STR, MEP
PAS 1192-5:2015 | M | Specification for security-minded building information modeling, digital built environments, and smart asset management | ARCH, STR, MEP
COBie (NBIMS US_V3_4.2) | M | Construction Operation Building Information Exchange | ARCH, STR, MEP
Uniclass 2015 | M | National Building Specification for Object Classification | ARCH, STR, MEP
ISO 5500:2014 | R | International Quality Standards | ARCH, STR, MEP
ISO BS EN 17412-1:2020 | M | Building Information Modelling. Level of Information Need. Concepts and principles | ARCH, STR, MEP

## Slide 25: BIM TEAM / STAKEHOLDERS
Name | Role | Orgnizaton | Location
Xavier Coll | Owner + Client | Client | Barcelona, Spain
Ayman Mahran | Structural Manager | Design | KSA
Billel Dridi | MEP Manager | Design | UAE
Omar Nasrallah | Architectural Manager | Design | KSA
Ammar Saud | BIM Manager | PMC | KSA
Mohamed Ezzat | BIM Coordinator | Supervision | KSA
Ahmed Khalaf | MEP Manager | Supervision | KSA

## Slide 26: BIM USES
BIM Goals | Description | Priority (High/Med/Low) | Plan/ Design/ Construct/ Operate |  |  | 
 |  |  | P | D | C | HO
Design Authoring | Providing the owner with powerful 3D visualization of the design with transparency ensures better collaboration and improves the quality control and quality assurance of the design, its cost, and schedule. | High | X | X | X | N/A
Design Reviews | Create different design options that meet the owner's needs and avoiding costly and timely traditional mock-ups. | High | N/A | X | X | N/A
3D Coordination | Coordinate the building project through a 3D model. To decrease construction time and cost, increase productivity, and get more accurate as-built drawings. | High | N/A | X | X | 
4D Phase Planning | Phase Planning | High | N/A | N/A | X | N/A
5D Cost Estimation | Provide the owner with a cost estimation schedule | Hight | X | X | X | 
Asset Management | Feed-in the Construction Operations Building Information Exchange(COBie) throughout the project life- cycle. Maintain up-to-date facility and equipment data including but not limited to maintenance schedules, warranties, cost data, upgrades, replacements, damages/deterioration, maintenance records, manufacturer's data, and equipment functionality. | Medium | N/A | X | X | 
Record Modeling | To provide the owner with an accurate and complete information model of the building, equipment, and spaces that can be useful for future renovation or equipment replacement. | High | N/A | N/A | N/A | 
Maintenance Scheduling | To effectively maintain building equipment through relying on preventive maintenance, avoiding costly corrective and emergency maintenance and improving the productivity of maintenance staff. | Medium | N/A | N/A | N/A | X

## Slide 27: MIDP
Master Information Delivery Plan
All Deliverables List

## Slide 28: TASK INFORMATION DELIVERY PLAN (TIDP)
 |  |  |  |  |  |  | Refer to file naming convention doc for info |  |  |  |  |  |  | 
 |  |  |  |  |  |  | File Naming Conventions |  |  |  |  |  |  | 
DESCRIPTION | EXCHANGE FORMATS |  |  |  |  |  | Project Code | Contract Code | Originat or Code | Volume / System | Levels/ Location s | Docume nt Type | Disci pline | Series Number
 | RVT | NWC | IFC | DWG | PDF | NWD |  |  |  |  |  |  |  | 
PLUMBING MODEL | X | X | X |  |  |  | KS012 | 987 | BON | ABC | ZZ | MOD | PL | 00001
PLUMBING - NOTES, LEGEND AND ABBREVIATIONS |  |  |  | X | X |  | KS012 | 987 | BON | ABC | ZZ | DWG | PL | 00001
PLUMBING - TYPICAL DETAILS SHEET-1 |  |  |  | X | X |  | KS012 | 987 | BON | ABC | ZZ | DWG | PL | 00001
GROUND FLOOR WATER SUPPLY LAYOUT |  |  |  | X | X |  | KS012 | 987 | BON | ABC | GF | DWG | PL | 00001
LEVEL 01 WATER SUPPLY LAYOUT |  |  |  | X | X |  | KS012 | 987 | BON | ABC | 01 | DWG | PL | 00001
LEVEL 02 WATER SUPPLY LAYOUT |  |  |  | X | X |  | KS012 | 987 | BON | ABC | 02 | DWG | PL | 00001
ROOF WATER SUPPLY LAYOUT |  |  |  | X | X |  | KS012 | 987 | BON | ABC | RF | DWG | PL | 00001

## Slide 29: TASK INFORMATION DELIVERY PLAN (TIDP)
 |  |  |  |  |  |  | Refer to file naming convention doc for info |  |  |  |  |  |  |  | DATA EXCHANGE #01 |  | DATA EXCHANGE #02 |  | DATA EXCHANGE #03 |  | DATA EXCHANGE #04 | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | STAGE: | Schematic Design | STAGE: | Schematic Design | STAGE: | Design Developme nt | STAGE: | Design Develop ment
 |  |  |  |  |  |  | File Naming Conventions |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Milestone: | 50% Schematic Design | Milestone: | 100% Schematic Design | Milestone: | 50% Design Developme nt | Milestone: | 100% Design Develop ment
DESCRIPTION | EXCHANGE FORMATS |  |  |  |  |  | Project Code | Contrac t Code | Origina tor Code | Volum e/ System | Levels/ Locatio ns | Docum ent Type | Disci pline | Series Numbe r | Discipline | DATE REQUIRED TO ISSUE | Discipline | DATE REQUIRED TO ISSUE | Discipline | DATE REQUIRED TO ISSUE | Discipline | DATE REQUIRE D TO ISSUE
 | RVT | NW C | IFC | DW G | PDF | NW D |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PLUMBING MODEL | X | X | X |  |  |  | KS012 | 987 | BON | ABC | ZZ | MOD | PL | 00001 | Mechanical Engineer | 1-Sep- 2022 | Mechanical Engineer | 16-Sep- 2022 | Mechanical Engineer | 1-Oct-2022 | Mechanical Engineer | 16-Oct- 2022
PLUMBING - NOTES, LEGEND AND ABBREVIATIONS |  |  |  | X | X |  | KS012 | 987 | BON | ABC | ZZ | DWG | PL | 00001 | Mechanical Engineer | 1-Sep- 2022 | Mechanical Engineer | 16-Sep- 2022 | Mechanical Engineer | 1-Oct-2022 | Mechanical Engineer | 16-Oct- 2022
PLUMBING - TYPICAL DETAILS SHEET-1 |  |  |  | X | X |  | KS012 | 987 | BON | ABC | ZZ | DWG | PL | 00001 | Mechanical Engineer | 1-Sep- 2022 | Mechanical Engineer | 16-Sep- 2022 | Mechanical Engineer | 1-Oct-2022 | Mechanical Engineer | 16-Oct- 2022
GROUND FLOOR WATER SUPPLY LAYOUT |  |  |  | X | X |  | KS012 | 987 | BON | ABC | GF | DWG | PL | 00001 | Mechanical Engineer | 1-Sep- 2022 | Mechanical Engineer | 16-Sep- 2022 | Mechanical Engineer | 1-Oct-2022 | Mechanical Engineer | 16-Oct- 2022
LEVEL 01 WATER SUPPLY LAYOUT |  |  |  | X | X |  | KS012 | 987 | BON | ABC | 01 | DWG | PL | 00001 | Mechanical Engineer | 1-Sep- 2022 | Mechanical Engineer | 16-Sep- 2022 | Mechanical Engineer | 1-Oct-2022 | Mechanical Engineer | 16-Oct- 2022
LEVEL 02 WATER SUPPLY LAYOUT |  |  |  | X | X |  | KS012 | 987 | BON | ABC | 02 | DWG | PL | 00001 | Mechanical Engineer | 1-Sep- 2022 | Mechanical Engineer | 16-Sep- 2022 | Mechanical Engineer | 1-Oct-2022 | Mechanical Engineer | 16-Oct- 2022
ROOF WATER SUPPLY LAYOUT |  |  |  | X | X |  | KS012 | 987 | BON | ABC | RF | DWG | PL | 00001 | Mechanical Engineer | 1-Sep- 2022 | Mechanical Engineer | 16-Sep- 2022 | Mechanical Engineer | 1-Oct-2022 | Mechanical Engineer | 16-Oct- 2022

## Slide 30: MASTER INFORMATION DELIVERY PLAN (MIDP) TIDP ARC
TIDP STR
TIDP PLP
TIDP MEC
TIDP ELE
MIDP

## Slide 31: FEDERATION STRATEGY

## Slide 32: LOIN

## Slide 33: CLASH MATRIX

## Slide 34: NAMING CONVENTION

## Slide 35: SOFTWARE
Use | Authoring Tool / Platform | Version
BIM Management Platform | Plannerly | Web Service
Data Management, Information exchange | BIMsync / One Drive | Web Service
Design / Construction Documents (Architecture) | Graphisoft Archicad | 2024 / 25
Design / Construction Documents (Structure) | Autodesk Revit | 2024
Design / Construction Documents (Civil) | Autodesk Revit / Tekla structure | 2024
Design / Construction Documents (MEP) | Autodesk Revit | 2024
3D Coordination / Clash Detection / Issue Management | BIMSync, BIMCollab Zoom, Solibiri | 2024
QTO | Solibiri | 2024
Model Validation | Solibiri ,BIMCollab Zoom | 2024
Cost Estimation | Solibiri, Excel | 2024
Site Collaboration | DALUX FIELD | Web Service

## Slide 36: MEETINGS
Meeting title | Description | Participants | Frequency | Location
Project Kick-off Meeting | Meeting to establish the principles of BIM adoption, scope, and ambition on the proposed project and to set up the post-contract-award BEP. Establish when and where future meetings will be held. | BIM manager BIM Coordinator MEP manager Architectural manager Structural manager | Single occurrence | Virtual
BIM workgroup meeting | Meeting to track the progress of BIM implementation on the project in the context of the BEP. This meeting should be used as a mechanism to identify forthcoming challenges and agree a proactive solution | BIM manager BIM Coordinator MEP manager Architectural manager Structural manager | Monthly | Virtual
BIM coordination meeting | Meeting to review and allocate responsibility to clashes found during the clash detection process undertaken | BIM manager BIM Coordinator MEP manager Architectural manager Structural manager | Weekly | Virtual
BIM validation meeting | Meeting to review and discuss deficiencies in model geometry and data identified during the model validation checks undertaken | BIM manager BIM Coordinator MEP manager Architectural manager Structural manager | Monthly–Aligned with BIM workgroup meetings | Virtual
BIM Use Progress Reviews | Metting to review and confirm BIM use progress aligned with project milestones. | BIM manager BIM Coordinator MEP manager Architectural manager Structural manager | Monthly / Weekly | Virtual
BIM Stage Closeout | Meeting to review and confirm project BIM deliverables according to EIR. | BIM manager BIM Coordinator MEP manager Architectural manager Structural manager | At Closeout Stage | Virtual

## Slide 37: SHARED COORDINATES
Physical Project Coordinates: |  | 
Project rotation from true north | 8.44° | 
Unit of measurement | metric units | 
Project Basepoint | E/W : 21611.1382 | N/S : 8971.0100
Project Elevation from sea level | 110 m | 
Project Survey Point | E/W : 21596.700 | N/S : 8971.7 00

## Slide 38: CHECKING/VALIDATION
Check that all families and worksets conform to standard naming conventions | 
Check that all objects are correctly classified in accordance with the BEP | 
Check that all objects contain the correct asset data appropriate to the design stage. | 
Check the file size should be checked according to the approved BEP | 
All extraneous drawing sheets, (i.e. those deemed to be not deliverable), have been removed from the BIM Model | 
Model external references (Xrefs) have been audited and purged | 
File format and naming conventions conforms to the EIR and remain constant for the lifespan of the project | 
Data segregation conforms to project requirements | 
3D and 2D drawings are up to date and that the 2D information has been derived from the model | 
All objects in a 3D default view must be made visible | 
All models to use the shared co-ordinate system defined at the outset of the project | 
Check the area and volume computations | 
Correct Grid and Level | 
Correct Model Category | 
Project Information is filled | 
Unused Linked cad Drawings to be removed | 
Check Project Base Point as per BEP | 

## Slide 39: QA/QC
Check model filename conforms to the BEP | 
Ensure model is detached from "Central" and audited while submitting on ACONEX | 
Update the model splash screen with correct revision and status etc. | 
Unload all links (do not remove the link) | 
Purge model (repeat process at least 3) | 
Check model is correctly assembled through visual inspection | 
Remove all non-required Views/Legends/Schedules/Sheets/Images | 
Check that all content is in the correct workset | 
Review and fix all warning messages where possible | 
Save model as next revision to CDE | 
Check & remove Object duplications | 
No in-place modelled families in the project | 
No 3D lines representing geometry should present in the model | 
Project points (survey and base points) should be checked according to the approved BEP | 
No filled region is used in drawing preparation to hide true model geometry | 
No design option should be used | 
Check model against floating elements, connectivity issues. | 
Visual appearance- no overlapping model element should present in the model | 

## Slide 40: BIM VIEW TEMPLATE

## Slide 41: INFORMATION REQUIREMENT
Client
Contractor
Contractor
Sub Contractor
Sub Contractor
More details
More details

## Slide 42: INFORMATION REQUIREMENT
Client
Contractor
Contractor
Sub Contractor
Sub Contractor
More details
More details

## Slide 43: INFORMATION REQUIREMENT
Appointing Party
Lead Appointed Party
Appointed Party
Appointed Party
Lead Appointed Party
More details
More details

## Slide 44: BEP
Sometimes it is required to submit pre-BEP in the bidding phase
Sometimes it is required to fill BIM assessment form
BEP is a live document (always Code B not A)

## Slide 45: BEP
For your reference:
cpix_post_contract_bim_execution_plan_bep_r1.0
cpix_pre-contract_bim_execution_plan_bep_v2.0
cpix_-_bim_assessment_form_ver_1.0

## Slide 47: CDE
Dear Ahmad
Please send me the last approved flooring drawings for ground floor
Best Regard
Dear Sami
Please find the attached file as
requested.
Best Regard
Dear Sami
Please find the attached new version of flooring drawings
Best Regard
Dear Sami
Please find the attached new revision of flooring drawings
Best Regard

## Slide 48
CDE

## Slide 49: CDE
Common Data Environment (CDE) is not about the software only. It is about the workflow
1- Define states of the information: Work in Progress, shared, published, and archived.
2- Classify the files by disciplines, assets, projects, authors, etc.
3- Revision numbering system, (Revision number – WIP or Shared)
4- Status codes that will reflect the suitability of the file; for review, coordination, information, etc.

## Slide 50
CDE

## Slide 51
CDE

## Slide 52
CDE

## Slide 53: BIM STANDARDS

## Slide 54: BIM STANDARDS
ISO 19650
https://bimportal.scottishfuturestrust.org.uk/level1/stage/8/task/47

## Slide 55: OPEN BIM
Open BIM is a universal approach to the collaborative design, realization, and operation of buildings based on open standards and workflows. (non- proprietary)
It is an initiative of several leading software vendors using the open building SMART Data Model.

## Slide 56: OPEN BIM
IFC
Not Issued for Construction 
Industry Foundation Class
Open BIM
Not to be edited
Similar to export to DXF

## Slide 57: OPEN BIM
BIM Collaboration Format
(BCF)

## Slide 58: COBIE CONSTRUCTION OPERATIONS BUILDING INFORMATION EXCHANGE
Project example explains it
Some clients require specific information documented as Asset Information Requirements (AIR)
COBie eBook: https://resources.prairieskyconsulting.com
/dorm-02/index.html

## Slide 59: COBIE CONSTRUCTION OPERATIONS BUILDING INFORMATION EXCHANGE

## Slide 60: COBIE CONSTRUCTION OPERATIONS BUILDING INFORMATION EXCHANGE
Type Example

## Slide 61: COBIE CONSTRUCTION OPERATIONS BUILDING INFORMATION EXCHANGE
Attached Documents such as Warranties

## Slide 62: COBIE CONSTRUCTION OPERATIONS BUILDING INFORMATION EXCHANGE
Components show where the type is installed in the whole project

## Slide 63
شكراً لإصغائكم
Thank you !
قائد نمذجة معلومات البناء
BIM Leader Diploma